| VALVE VOLTMETER Circuit Code for Dwg. Nos. 8400D7 8400D14 | AMALGAMATED WIRELESS (AUSTRALASIA) LTD - SYDNEY |
| --- | --- |
| APP. | CKD. | TRCD. | DRN. | ARGT. | REF. |
|  |  |  |  |  | 1ST SHEET REF. |
| DRG. 8400D8 | 4M8400 TYPE 5M8400 6M8400 | 1 |
|  |  | 2 |
|  |  | 3 |
|  |  | 4 |
|  |  | 5 |
|  |  | ` |

| VALVE VOLTMETER Circuit Code for Dwg. Nos. 8400D7 8400D14 | AMALGAMATED WIRELESS (AUSTRALASIA) LTD - SYDNEY |
| --- | --- |
| APP. | CKD. | TRCD. | DRN. | ARGT. | REF. |
|  |  |  |  |  | 1ST SHEET REF. |
| DRG. 8400D9 | 4M8400 TYPE 5M8400 6M8400 | 1 |
|  |  | 2 |
|  |  | 3 |
|  |  | 4 |
|  |  | 5 |

| VALVE VOLTMETER Circuit Code for Dwg. Nos. 8400D7 8400D14 | AMALGAMATED WIRELESS (AUSTRALASIA) LTD - SYDNEY |
| --- | --- |
| APP. | CKD. | TRCD. | DRN. | ARGT. | REF. |
|  |  |  |  |  | 1ST SHEET REF. |
| DRG. 8400D10 | 4M8400 TYPE 5M8400 6M8400 | 1 |
|  |  | 2 |
|  |  | 3 |
|  |  | 4 |
|  |  | 5 |

| VALVE VOLTMETER Circuit Code for Dwg. Nos. 8400D7 8400D14 | AMALGAMATED WIRELESS (AUSTRALASIA) LTD - SYDNEY |
| --- | --- |
| APP. | CKD. | TRCD. | DRN. | ARGT. | REF. |
|  |  |  |  |  | 1ST SHEET REF. |
| DRG. 8400D11 | 4M8400 TYPE 5M8400 6M8400 | 1 |
|  |  | 2 |
|  |  | 3 |
|  |  | 4 |
|  |  | 5 |

| VALVE VOLTMETER Circuit Code for Dwg. Nos. 8400D7 8400D14 | AMALGAMATED WIRELESS (AUSTRALASIA) LTD - SYDNEY |
| --- | --- |
| APP. | CKD. | TRCD. | DRN. | ARGT. | REF. |
|  |  |  |  |  | 1ST SHEET REF. |
| DRG. 8400D12 | 4M8400 TYPE 5M8400 6M8400 | 1 |
|  |  | 2 |
|  |  | 3 |
|  |  | 4 |
|  |  | 5 |

| INPUT IMPEDANCE V FREQUENCY SERIES M8400 | AMALGAMATED WIRELESS (AUSTRALASIA) LTD - SYDNEY |
| --- | --- |
| APP. | CKD. | TRCD. | DRN. | ARGT. | REF. |
|  |  |  |  |  | 1ST SHEET REF. |
| DRG. 8400D16 | TYPE SERIES M8400 | 1 |
|  |  | 2 |
|  |  | 3 |
|  |  | 4 |
|  |  | 5 |

# Text boxes

Item		Circ.

No.		Ref.				Description		             Manufacturer	   A.W.A. Type   	      RESISTORS:			       	                                                      Name.	Design.	    or Ref. No.

5251	R1	5MΩ  1W. carbon, insulated	IRC	BT1	600755

5245	R2	5,000Ω 1W. carbon, insulated	IRC	BT1	600695

5246	R3	25,000Ω 1W. carbon, insulated	IRC	BT1	600709

5246(	R4	0.125 MΩ 2W. (0.1MΩ 1W, 0.25MΩ 1W carbon,	IRC	BT`	600721

5247(		 insulated in series)			600709

5248(

5248	R5	0.4MΩ 1/2W carbon, non-insulated	Chanex	RR4041	600333

5249	R6	1.6 MΩ 1W carbon, insulated	IRC	BT1	600745

5254	R7	50,000Ω 1W carbon, insulated	IRC	BT1	600715

6049	R8	0.5MΩ carbon, potentiometer	Aerostat		8400D6

5250	R9	0.1MΩ 2W carbon, insulated	IRC	BT2	600921

----	R10	Not used

6041	R11	50,000Ω carbon potentiometer			8400D4

6048	R12	25,000Ω carbon potentiometer			8400D5

6048	R13	25,000Ω carbon potentiometer			8400D5

7030	R14	3,000Ω w.w. Potentiometer	AWA                        8400T7030

7030	R15	3,000Ω w.w. Potentiometer	AWA	            8400T7030

7021	R16	5,000Ω w.w. Potentiometer	AWA		  S5711

7021	R17	5,000Ω w.w. Potentiometer	AWA		  S5711

7021	R18	5,000Ω w.w. Potentiometer	AWA		  S5711

Item		Circ.

No.		Ref.				Description		             Manufacturer	   A.W.A. Type   	      RESISTORS:			       	                                                                   Name.	Design.	    or Ref. No.

7021	R19	5,000Ω w.w. Potentiometer	AWA		  S5711

7021	R20	5,000Ω w.w. Potentiometer	AWA		  S5711

-----	R21	Not Used

5243	R22	0.32MΩ 1W carbon, insulated	IRC	BT1	600731

5244	R23	0.25MΩ 1W carbon, insulated	IRC	BT1	600729

5244	R24	0.25MΩ 1W carbon, insulated	IRC	BT1	600729

5254	R25	50,000Ω 1W carbon, insulated	IRC	BT1	600715

6042	R26	10,000Ω 12.5W, Term.2, w.w. type DJ,ctg.C	IRC		605301

6043	R27	20,000Ω (2 x 10,000Ω 5W type AB ctg.C	IRC	BTI	602901

Term. 1 w.w. in series)

6044	R28	7,500Ω 5W type AB ctg. C Term.1 w.w.	IRC

6045	R29	2,500Ω 3W type AA ctg.  C.Term.1 w.w.	IRC		602389

6046	R30	750Ω 3W type AA ctg. C term.1 w.w.	IRC

6047	R31	200Ω 3W type AA ctg. C Term.1 w.w.	IRC		602367

5252	R32	200 1W carbon, non-insulated	Chanex	RM2011	600467

5252	R33	200 1W carbon, non-insulated	Chanex	RM2011	600467

6052	R34	100Ω 3W type AA ctg. C term.1	IRC		602361

(used on type 6M8400 only)

6052	R35	100Ω 3W type AA ctg. C term.1	IRC		602361

(used on type 6M8400 only)

Item		Circ.

No.		Ref.				Description		                  Manufacturer	         A.W.A. Type   	      			       	                                                                            Name.  Design.          or Ref. No.

RESISTORS:

3414	R36	0.043Ω 8 turns No. 10 Eureka En. Wire	AWA		8400V3414

(used on type 6M8400 only)

CONDENSERS:

6054	C1	0.01µF 500VWDC Mica Dielectric	Simplex	SM	224501

6054	C2	0.01µF 500VWDC Mica Dielectric	Simplex	SM	224501

6054	C3	0.01µF 500VWDC Mica Dielectric	Simplex	SM	224501

6059	C4	25µF 40VPDC Electrolytic	Ducon	ET10769

5211	C5	0.5µF 350VWDC paper Dielectric	AWA		228135

5211	C6	0.5µF 350VWDC paper Dielectric	AWA		228135

6058	C7	2.0µF 350VWDC paper Dielectric	Ducon		U7955

6058	C8	2.0µF 350VWDC paper Dielectric	Ducon		U7955

6057	C9	25µF 40VPDC Electrolytic	Ducon	EE10779

6056	C10	8.0 µF 600 VPDC Electrolytic	Ducon	EE10577

6056	C11	8.0 µF 600 VPDC Electrolytic	Ducon	EE10577

6056	C12	8.0 µF 600 VPDC Electrolytic	Ducon	EE10577

6054	C13	0.01µF 500VWDC Mica Dielectric	Simplex	SM	224501

(used on type 6M8400 only)

6054	C14	0.01µF 500VWDC Mica Dielectric	Simplex	SM	224501

(used on type 6M8400 only)

Item		Circ.

No.		Ref.				Description		             Manufacturer	   A.W.A. Type   	      RESISTORS:			       	                                                      Name.	Design.	    or Ref. No.

TRANSFORMERS: (contd.)

7026	T1	220-260V input 40-60 c/s 5V 2 amp. 6.3V 1.1 amp. 	AWA	                	1TJ7447

310V-0-310V 20 mA output. Metal tank 2.3/4” x 4”

x 3.1/4” x 4.1/16” high.

(used on type 5M8400 only)

7027	T1	Vib. Transf. 6V (mod.)	AWA		1TJ8479

INDUCTORS:

7015	L1	Vibrator Filter Choke	AWA	         Prod.Pt. 8569

(used on type 6M8400 only)

7016	L2	R.F. Choke	AWA                      Prod.Pt. 3036

SWITCHES:

2124	S1	Switch	AWA	           8400T2124

7014	S2	3 wafers, 2 x 2 pole, 5-pos. 1 x 1 pole 5-pos.	AWA,Oak	“H”          8400D2

5277	S3	Switch, S.P.D.T.	Alpha	Toggle	S3510

LAMP:

5231	PL1	Pilot Lamp 6.3V 0.35 amp.	Mazda	46

METERS:

6027	m1	Meter 0-75µA		Simpson 	75	471000

Item		Circ.

No.		Ref.				Description		             Manufacturer	   A.W.A. Type   	      RESISTORS:			       	                                                      Name.	Design.	    or Ref. No.

C15	0.01µF 500VWDC Mica Dielectric	Simplex	SM	224501

(used on type 6M8400 only)

C16	0.01µF 500VWDC Mica Dielectric	Simplex	SM	224501

(used on type 6M8400 only)

C17	0.01µF 500VWDC Mica Dielectric	Simplex	SM	224501

(used on type 6M8400 only)

VALVES:

6025	V1	Detector								Rad.			9072

6023	V2	Full wave Rectifier						Rad.		        6X5GT		(not used on 6M8400)

6024	V3	Regulator							Rad.		    VR150-30

VIBRATORS:

7028	VIB.1 6V Synchronous							AWA		        H7220

(used on 6M8400 only)

TRANSFORMERS:

7025	T1	220-260V input 40-60 c/s 5V 2 amp. 6.3V 1.1 amp. 			AWA		     3TJ7447

310V-0-310V 20 mA output. Metal tank 2.1/2” x 4”

x 4.7/8” high.

(used on type 4M8400 only)